## Slide 1
MIE 402 | MECHANICAL ENGINEERING LABORATORY II
Orientation and
report writing
Fall 2026 · Prof. Ehsan Roohi September 9, 2026
MEASURE
MODEL
COMPARE
Notes: TIME: 0–1 minutes (1 minutes)
Welcome students. Today prepares you to collect useful evidence and write the four reports required this semester. Ask: If two groups report different frequencies for the same apparatus, what information would help you decide whether either result is trustworthy? Take two brief answers. Explain that the session includes a tour of all six experiments, a detailed report walkthrough, and a short exercise. The report template and syllabus are available on the course site.
SOURCE: Syllabus_MIE402_Fall26_6Labs.pdf and supplied Lecture 01
Report instructions: Template for MIE 402 Report.docx. Teaching examples labeled illustrative use invented values.

## Slide 2
MIE 402 | ME LAB II
Experimental evidence and engineering judgment
2
01
OBSERVE
See the physical behavior worth explaining
→
02
MEASURE
Acquire data with a deliberate measurement system
→
03
COMPARE
Test data against theory and models
→
04
COMMUNICATE
Write a report another engineer can trust
The goal is not merely to collect numbers. The goal is to make a claim that the data support.
Notes: TIME: 1–1.5 minutes (0.5 minutes)
Connect the four stages to the opening question. A believable number needs a measurement method, units, a model with stated assumptions, and an estimate of what might change the conclusion. The report is the record of that reasoning.
SOURCE: Syllabus_MIE402_Fall26_6Labs.pdf and supplied Lecture 01
Report instructions: Template for MIE 402 Report.docx. Teaching examples labeled illustrative use invented values.

## Slide 3
MIE 402 | ME LAB II
Today’s 50-minute session
3
01
0–8 min: course organization and workflow
02
8–20 min: six experiments and their evidence
03
20–42 min: report writing and comparison
04
42–48 min: policies and report exercise
05
48–50 min: first dates and preparation
Notes: TIME: 1.5–2 minutes (0.5 minutes)
Preview the timing. Tell students that the six experiment introductions are conceptual previews. Detailed procedures and pre-lab requirements come with each experiment. Reserve the exercise time so students practice the distinction between reporting an observation and explaining it.
SOURCE: Syllabus_MIE402_Fall26_6Labs.pdf and supplied Lecture 01
Report instructions: Template for MIE 402 Report.docx. Teaching examples labeled illustrative use invented values.

## Slide 4
MIE 402 | ME LAB II
People, places, and weekly rhythm
4
COURSE TEAM
Prof. Ehsan Roohi
Yuyuan Zhang
Nazila Emamdoost
WEEKLY RHYTHM
MON
Theory • 12:20–1:10 PM
Hasbrouck Laboratory 134
TUE–FRI
Laboratory sections
Gunness Laboratory 5
FRI
Office hours • 12:20–1:10 PM
Gunness Laboratory 1
Check Canvas for your assigned section, GTA, and any section-specific updates.
Notes: TIME: 2–4 minutes (2 minutes)
Introduce the two GTAs, Yuyuan Zhang and Nazila Emamdoost. Ask students to check their own section and GTA in Canvas. September 9 is a one-time Wednesday orientation. Regular theory meetings are on Mondays. There is no regular Wednesday theory meeting. Explain the difference between the 50-minute theory meeting and the scheduled laboratory section. General questions belong in lecture, individual questions in office hours, and email is appropriate when those options are not practical.
SOURCE: Syllabus_MIE402_Fall26_6Labs.pdf and supplied Lecture 01
Report instructions: Template for MIE 402 Report.docx. Teaching examples labeled illustrative use invented values.

## Slide 5
MIE 402 | ME LAB II
Course grading
5
Chart: 
| Pre-labs | Lab 1 report | Labs 2+3 | Labs 4+5 | Lab 6 report | Participation
Weight | 20 | 10 | 25 | 25 | 15 | 5
100%
Preparation + reports + participation
The combined reports reward synthesis across related experiments.
Notes: TIME: 4–6 minutes (2 minutes)
Reports account for 75% of the course grade, six pre-labs account for 20%, and participation accounts for 5%. There are four report submissions, not six separate reports. Each combined report should connect its two experiments. Distinguish these course weights from the report rubric: the rubric allocates ten equally weighted criteria within each report. Pre-labs prepare the theory and analysis needed for a productive lab session. Report dates are tentative and Canvas carries updates.
SOURCE: Syllabus_MIE402_Fall26_6Labs.pdf and supplied Lecture 01
Report instructions: Template for MIE 402 Report.docx. Teaching examples labeled illustrative use invented values.

## Slide 6
MIE 402 | ME LAB II
The laboratory workflow
6
PRE-LAB
Build the theory and analysis tools before arriving
→
LAB
Acquire data, check quality, and document the method
→
ANALYSIS
Process data, quantify uncertainty, compare cases
→
REPORT
Make a clear claim and support it with evidence
Pre-labs are due before your own laboratory section begins.
Notes: TIME: 6–7 minutes (1 minutes)
Walk through a concrete example: before the pendulum lab, establish the equation and expected period. During the lab, record the initial angle, geometry, frame rate, and motion. Afterward, keep raw data unchanged and use a traceable analysis to generate the report figures. Check at least one data set before leaving the laboratory so a missing file or poor recording does not become a report-writing problem.
SOURCE: Syllabus_MIE402_Fall26_6Labs.pdf and supplied Lecture 01
Report instructions: Template for MIE 402 Report.docx. Teaching examples labeled illustrative use invented values.

## Slide 7
MIE 402 | ME LAB II
Six experiments and four reports
7
Lab | Experiment | Primary focus | Report
1 | Dynamic data sampling | Sampling, aliasing, spectra | Lab 1
2 | Single pendulum | Dynamic response, model–data | Labs 2+3
3 | Double pendulum | Coupled and nonlinear motion | Labs 2+3
4 | 1-DOF free response | Natural frequency, damping | Labs 4+5
5 | 1-DOF forced response | Resonance, frequency response | Labs 4+5
6 | Radiometer | Movement measurement | Lab 6
Notes: TIME: 7–8 minutes (1 minutes)
Use the Fall 2026 numbering. Lab 6 is the radiometer. Older course files use Lab 6 for a different apparatus, so direct students to the current Canvas release. The sequence begins with the reliability of measurements, continues through simple and coupled dynamics, and ends with rotation driven by thermal effects. The next six slides describe the measurement question and report evidence for each experiment.
SOURCE: Syllabus_MIE402_Fall26_6Labs.pdf and supplied Lecture 01
Report instructions: Template for MIE 402 Report.docx. Teaching examples labeled illustrative use invented values.

## Slide 8
MIE 402 | ME LAB II
Lab 1: Sampling and frequency analysis
Question
How can the same sound produce different sampled signals?
Measurement
Record microphone voltage and the sampling rate. Compare time traces and spectra.
Report evidence
Show how sample rate and record duration affect the inferred frequency. Identify aliasing.
fₛ > 2 fmax Δf = fₛ / N = 1 / Trecord
The Nyquist condition assumes a band-limited input. Practical acquisition needs filtering and margin.
8
Notes: TIME: 8–10 minutes (2 minutes)
Explain that the sensor produces a time signal but the computer stores only selected samples. For an illustrative 100 Hz tone, 150 samples per second can make it appear as a 50 Hz component, while 1000 samples per second represents the oscillation much better. Ask whether taking more samples at the same inadequate sampling rate removes aliasing. It does not. A longer record gives finer FFT-bin spacing, while a sufficiently high sample rate addresses the sampling limit. Keep sampling rate and record length distinct. The report should compare traces and spectra with axes, units, and acquisition settings. This is a preview, not a substitute for the released procedure.
SOURCE: LAB1_MIE402.pdf
Report instructions: Template for MIE 402 Report.docx. Teaching examples labeled illustrative use invented values.

## Slide 9
MIE 402 | ME LAB II
Lab 2: Single pendulum
Question
When does a small-angle model predict the measured motion?
Measurement
Track angle from video. Record geometry, mass properties, frame rate, and release angle.
Report evidence
Compare measured and predicted angle histories and periods for small and larger releases.
Iₚ θ̈ + m g d sin θ = 0 Tsmall = 2π √(Iₚ / m g d)
Iₚ is inertia about the pivot. d is the pivot-to-center-of-mass distance. The model neglects losses.
9
Notes: TIME: 10–12 minutes (2 minutes)
The actual pendulum contains distributed mass, so do not automatically use the point-mass formula with the rod length. Identify the moment of inertia about the pivot and the center-of-mass distance. For small angular displacement in radians, sin(theta) is approximately theta. Ask students what could change at larger release angles: the linear approximation, and therefore the predicted period. The supplied procedure uses several release-angle ranges and video tracking. Compare the correct initial conditions in the experiment and simulation. A decrease in amplitude can indicate losses absent from the ideal undamped equation. Save the video calibration and angle convention.
SOURCE: LAB2_MIE402.pdf
Report instructions: Template for MIE 402 Report.docx. Teaching examples labeled illustrative use invented values.

## Slide 10
MIE 402 | ME LAB II
Lab 3: Double pendulum
Question
How does coupling change the motion of two connected bodies?
Measurement
Track both angles and record both initial angles and release conditions.
Report evidence
Overlay measured and simulated angle histories. Compare small and large motions and their spectra.
Trajectory divergence alone does not establish chaos. Check initial conditions, tracking, and model assumptions.
10
Notes: TIME: 12–14 minutes (2 minutes)
A second angle introduces coupling: the motion of one link influences the other. At small amplitudes, students can look for coupled oscillatory behavior and multiple characteristic frequencies. At larger amplitudes, nonlinear behavior makes a single sinusoidal description inadequate and trajectories can become sensitive to initial conditions. Avoid promising that every trial is chaotic. Ask whether a late mismatch between measured and simulated trajectories automatically means a numerical solver is wrong. Possible causes include a small initial-angle mismatch, uncertain mass properties, unmodeled friction, and image-tracking error. The report should show both angles with clear definitions and time alignment.
SOURCE: LAB3_MIE402.pdf
Report instructions: Template for MIE 402 Report.docx. Teaching examples labeled illustrative use invented values.

## Slide 11
MIE 402 | ME LAB II
Lab 4: Free response of a 1-DOF system
Question
What do oscillation period and amplitude decay reveal about the system?
Measurement
Displace the cart and release it. Measure mass, effective stiffness, and displacement versus time.
Report evidence
Estimate natural frequency and damping. Compare cases with changed mass, springs, or damping.
m ẍ + c ẋ + k x = 0 ωn = √(k / m) ζ = c / (2√(k m))
For an underdamped viscous model, ωd = ωn √(1 − ζ²). Natural and damped frequency differ.
11
Notes: TIME: 14–16 minutes (2 minutes)
Use the terms carefully. A free response starts from an initial condition without continued excitation. The oscillation period primarily reflects mass and stiffness, while the envelope decay reflects damping. Ask students to predict what happens when mass increases while stiffness stays fixed: the natural frequency decreases. Keep the effective system stiffness consistent with the spring arrangement. For an underdamped response, the peak spacing gives the damped frequency. A logarithmic decrement can estimate damping when the viscous model and clean peak data are appropriate. Students should explain how they selected peaks, removed equilibrium offsets, and compared multiple configurations.
SOURCE: LAB4_MIE402.pdf
Report instructions: Template for MIE 402 Report.docx. Teaching examples labeled illustrative use invented values.

## Slide 12
MIE 402 | ME LAB II
Lab 5: Forced response of a 1-DOF system
Question
How does excitation frequency affect response amplitude and phase?
Measurement
Apply the assigned impulse and harmonic inputs. Record input motion or force and the cart response.
Report evidence
Separate the transient from the periodic response. Plot amplitude or gain against excitation frequency.
m ẍ + c ẋ + k x = F(t)
This is the force-input model. A moving spring attachment requires the corresponding base-motion input model.
12
Notes: TIME: 16–18 minutes (2 minutes)
Explain the difference between free decay and sustained forcing. Near resonance, a lightly damped system can respond strongly. Ask why a measurement immediately after changing excitation frequency might be misleading: transient motion remains. The supplied apparatus includes motion of a spring attachment, so students must identify whether they measure force or base displacement and choose the matching input-output model. Record input amplitude at every frequency rather than assuming it remains constant. For the combined report, use the Lab 4 estimates as an independent check on the Lab 5 response wherever the configuration is the same. Document changes to springs, mass, or damping before comparing parameters.
SOURCE: LAB5_MIE402.pdf
Report instructions: Template for MIE 402 Report.docx. Teaching examples labeled illustrative use invented values.

## Slide 13
MIE 402 | ME LAB II
Lab 6: Radiometer rotation
Question
How does illumination relate to measured rotation over a controlled time window?
Measurement
Track cumulative angle from video. Record illuminance, light position, and thermal history.
Report evidence
Fit angle versus time to estimate RPM. Compare identical measurement windows and discuss warming.
θ(t) ≈ θ₀ + ωavg t RPM = (60 / 2π) ωavg
ωavg is in rad/s. Lux measures illuminance, not absorbed heating power.
13
Notes: TIME: 18–20 minutes (2 minutes)
The black and reflective vane surfaces interact differently with radiation. Temperature differences and rarefied-gas transport generate the observed torque. Ordinary photon-pressure reasoning does not explain the typical Crookes radiometer rotation. Keep the first lecture focused on the measurable output: cumulative angle and an average slope over a stated interval. Differentiating noisy frame-by-frame angles can produce misleading speed spikes. Use the same elapsed-time window when comparing cases and record whether later runs start warm. The available module discusses thermal slowdown and an optional first-order rotational model. Do not demand a precise Knudsen number from an unknown internal gas pressure. Follow the released procedure and instructor guidance for lamp placement and glass handling.
SOURCE: Radiometer Test/Crookes_Radiometer_Laboratory_Module__Rarefied_Gas_Transport__Light_Driven_Rotation__and_Video_Based_RPM_Measurement.pdf
Report instructions: Template for MIE 402 Report.docx. Teaching examples labeled illustrative use invented values.

## Slide 14
MIE 402 | ME LAB II
The structure of a laboratory report
14
REQUIRED SECTIONS
Abstract
1. Introduction
2. Method
3. Results
4. Comparison
5. Discussion
6. Conclusions
References • Appendices
WHAT THE READER SHOULD FIND
• A clear purpose and relevant theory
• A reproducible method
• Readable figures with units and labels
• Direct comparison with theory or a model
• A discussion of discrepancies and limitations
• Conclusions supported by the presented data
Meaningful results matter more than a polished page with weak analysis.
Notes: TIME: 20–22 minutes (2 minutes)
Open the actual report template or point students to its download link. Explain the reader: someone with relevant undergraduate background who was not present during the experiment. The report must answer what you studied, how you measured it, what happened, how it compares with a prediction, and what the comparison means. References are required, including the lecture notes at minimum. An appendix is optional and cannot replace evidence needed for the main conclusion. Explain the difference between the report outline and the grading rubric: having each section earns only one of the ten rubric categories.
SOURCE: Syllabus_MIE402_Fall26_6Labs.pdf and supplied Lecture 01
Report instructions: Template for MIE 402 Report.docx. Teaching examples labeled illustrative use invented values.

## Slide 15
MIE 402 | ME LAB II
Report length and section purpose
Section | Template allocation | Main purpose
Abstract | Maximum 10 lines | Purpose, method, key finding, implication
Introduction | 1 page | Theory, experiment, and testable objective
Method | 1 page | Enough detail to reproduce the measurement
Results | 3 pages including figures | Observed behavior and processed measurements
Comparison | 1 page | Prediction and experiment on the same basis
Discussion | 1 page | Discrepancies, uncertainty, and limitations
Conclusions | 1 page | Quantitative answer and the main lesson
References and optional appendices have no stated page limit. Follow any assignment-specific limit on Canvas.
15
Notes: TIME: 22–24 minutes (2 minutes)
The template provides section-level allocations, including a maximum of ten lines for the abstract. The numbered main sections total eight pages, with three of those pages reserved for results and figures. Do not announce an invented overall page limit that includes the cover and references. Do not assume a combined report doubles the allocation. Follow the stated limit for each assignment. These lengths encourage selection: include the evidence needed for the claim, rather than every plot generated. Remind students to put group members in alphabetical order by last name as directed by the cover template.
SOURCE: Template for MIE 402 Report.docx
Report instructions: Template for MIE 402 Report.docx. Teaching examples labeled illustrative use invented values.

## Slide 16
MIE 402 | ME LAB II
Introduction and reproducible method
Introduction
State a testable objective. Give the governing equation, define symbols, and explain assumptions.
Method
Describe the actual apparatus, calibration, sampling settings, initial conditions, and repeated runs.
Analysis record
Explain processing choices, fitting intervals, and parameter sources so another person can repeat the analysis.
Example objective: test how release angle changes agreement with the small-angle pendulum model.
16
Notes: TIME: 24–26 minutes (2 minutes)
An introduction should establish the experiment and the relevant theory without copying a textbook chapter. For a pendulum, identify the angle convention, inertia, geometry, and the approximation under test. The method should describe what the group actually did. Include sensor or camera settings and calibration, not every button pressed. Show how measured quantities become the reported quantity: pixels become position, position becomes angle, and peak times become period. State how many runs you made and what changed between them. If you filtered data, explain the filter and its possible effect. Keep original data and scripts so every final figure has a traceable origin.
SOURCE: Template for MIE 402 Report.docx
Report instructions: Template for MIE 402 Report.docx. Teaching examples labeled illustrative use invented values.

## Slide 17
MIE 402 | ME LAB II
A concise, quantitative abstract
Purpose and method
We tested a small-angle pendulum prediction using angle histories from video.
Key result
The measured frequency was 1.47 Hz, compared with a predicted 1.50 Hz, a 2.0% difference.
Meaning and limit
The agreement supports the model for this case. The discrepancy requires an uncertainty assessment.
Illustrative wording and invented teaching values. An actual abstract must use your own results. Maximum 10 lines.
17
Notes: TIME: 26–28 minutes (2 minutes)
Read the three parts aloud and identify the role of each. A useful abstract tells the reader the purpose, what was done, the most important numerical result, and the implication. It should be written after the analysis and conclusions so the numbers agree across the report. The values here are invented for teaching, not a result from this course apparatus. A two-percent difference by itself does not prove agreement within uncertainty. If your actual report supports an uncertainty statement, include it precisely. Avoid an abstract that only lists activities, such as saying that a pendulum was released and graphs were plotted.
SOURCE: Template for MIE 402 Report.docx
Report instructions: Template for MIE 402 Report.docx. Teaching examples labeled illustrative use invented values.

## Slide 18
MIE 402 | ME LAB II
Results: the measured behavior
Observation
Describe what the measurements show, with quantities and units.
Evidence
Use figures or tables that answer the experimental question. Identify conditions and repeated runs.
Traceability
Distinguish measured data, processed measurements, and simulation predictions.
Example observation: successive positive displacement peaks decrease over time.
18
Notes: TIME: 28–29 minutes (1 minutes)
Results present what happened. A plot of a simulated trajectory alone cannot stand in for the measured response of a physical experiment. Identify processing without hiding its effect. Explain the trend and point to the relevant figure rather than saying only that the results are shown below. Save causal explanations for the Discussion, while keeping enough context for the reader to understand each measurement.
SOURCE: Template for MIE 402 Report.docx
Report instructions: Template for MIE 402 Report.docx. Teaching examples labeled illustrative use invented values.

## Slide 19
MIE 402 | ME LAB II
Readable, exported figures
19
DO
• Export high-resolution PNG, EPS, or PDF
• Label axes and include units
• Use legends that identify each data set
• Group related cases when comparison improves the analysis
AVOID
• Screenshots of MATLAB or Python figure windows
• Tiny labels and unreadable legends
• Decorative plots that do not answer a question
• Separate figures when one comparison plot is clearer
A figure should still make sense when viewed without the surrounding paragraph.
Notes: TIME: 29–30 minutes (1 minutes)
Use the syllabus export rule when preparing the final report. The older template mentions copying a figure, but the final result must still be a clean, readable figure without application-window chrome. A figure needs context: the apparatus or case, acquisition settings where relevant, and the distinction between experiment and prediction. Color alone may be insufficient, so combine color with markers or line styles. Verify quality in the PDF because a figure that looks fine in the editor can become tiny or rasterized on export.
SOURCE: Syllabus_MIE402_Fall26_6Labs.pdf and supplied Lecture 01
Report instructions: Template for MIE 402 Report.docx. Teaching examples labeled illustrative use invented values.

## Slide 20
MIE 402 | ME LAB II
A figure that supports a comparison
Chart: Angle (degrees)
Figure 1. Illustrative angle histories: undamped model and synthetic decaying signal, 5° initial angle, 50 samples/s.
20
Notes: TIME: 30–32 minutes (2 minutes)
This is a deliberately simplified teaching figure using synthetic data. Both series use the same time origin and angle convention. The model is 5 cos(2 pi 1.50 t) degrees. The synthetic signal is 5 exp(-0.45 t) cos(2 pi 1.47 t) degrees, sampled at 50 Hz. Ask students to identify one observed difference before proposing a cause. The decaying envelope is visible, and a slight phase drift grows over time. The caption states the conditions, the axes include units, and the legend identifies both series. A good figure supports a specific statement. It does not, by itself, establish why a discrepancy occurred.
SOURCE: Syllabus_MIE402_Fall26_6Labs.pdf and supplied Lecture 01
Report instructions: Template for MIE 402 Report.docx. Teaching examples labeled illustrative use invented values.

## Slide 21
MIE 402 | ME LAB II
Comparison: a fair test of the model
Same basis
Use matching units, initial conditions, time origin, and system parameters. Explain the theoretical solution.
Quantitative comparison
Compare period, frequency, amplitude, phase, damping, or another quantity relevant to the objective.
Parameter honesty
State which parameters you measured, assumed, or fitted. A fit to the same data is not independent validation.
Relative discrepancy = | measured − predicted | / | predicted | × 100%
Use an appropriate absolute or scaled metric when the predicted value is zero or very small.
21
Notes: TIME: 32–34 minutes (2 minutes)
Return to the 1.47 Hz versus 1.50 Hz example. The absolute difference is 0.03 Hz and the relative discrepancy is two percent using the predicted value as the reference. A single number can miss a time-dependent mismatch, so also inspect an overlay or residual where appropriate. Do not repeatedly shift a simulation or tune parameters without reporting that choice. If damping was estimated from the same decay record used for the comparison, describe the result as a fitted-model agreement. An independent trial or a different response can test how well the fitted parameters generalize. The equations belong in the Introduction and the solution procedure and parameter values belong in the Comparison.
SOURCE: Template for MIE 402 Report.docx
Report instructions: Template for MIE 402 Report.docx. Teaching examples labeled illustrative use invented values.

## Slide 22
MIE 402 | ME LAB II
Uncertainty and acceptable agreement
Measurement uncertainty
Consider calibration, resolution, repeatability, timing, and tracking choices.
Model uncertainty
Consider uncertain parameters and omitted physics, such as friction or large-angle effects.
A justified conclusion
Report what each uncertainty means. Compare the discrepancy with a consistent uncertainty estimate.
T = Δt / ncycles uT ≈ uΔt / ncycles
Simplified timing example with exact cycle count. Longer timing intervals do not remove calibration bias.
22
Notes: TIME: 34–36 minutes (2 minutes)
Ask whether a two-percent discrepancy is acceptable. The answer depends on the measurement and model uncertainty and the intended use. If two independent standard uncertainties were 0.02 Hz each, their combined standard uncertainty would be sqrt(0.02 squared plus 0.02 squared), about 0.028 Hz. The 0.03 Hz discrepancy would be about 1.1 combined standard uncertainties. This is a classroom illustration, not a formal acceptance criterion. A plus/minus value must state whether it is instrument resolution, run-to-run standard deviation, uncertainty of a mean, or a confidence interval. Timing several cycles can reduce the relative effect of endpoint timing error, but it does not remove a biased clock or incorrect length calibration.
SOURCE: Syllabus_MIE402_Fall26_6Labs.pdf and supplied Lecture 01
Report instructions: Template for MIE 402 Report.docx. Teaching examples labeled illustrative use invented values.

## Slide 23
MIE 402 | ME LAB II
Discussion: explanations tied to evidence
Observed difference
The measured oscillation envelope decays while the undamped prediction keeps constant amplitude.
Plausible mechanism
Friction or drag could dissipate energy. The present comparison does not identify their separate contributions.
Discriminating check
Compare decay across configurations and test whether the chosen damping model describes the envelope.
Replace “human error” with a specific mechanism, its expected effect, and a way to check it.
23
Notes: TIME: 36–38 minutes (2 minutes)
Explain why this paragraph is stronger than saying the experiment differed because of human error. It describes a visible feature, proposes a mechanism consistent with that feature, and identifies a further check. Plausibility is not proof. Students should explain the direction and scale of an effect where possible. A wrong frame rate changes time and frequency estimates. A length-calibration error changes positions or inferred model parameters. A delayed time origin changes phase. Random tracking scatter has a different signature from systematic drift. Discuss whether the evidence supports the model over the tested range and where that conclusion stops.
SOURCE: Template for MIE 402 Report.docx
Report instructions: Template for MIE 402 Report.docx. Teaching examples labeled illustrative use invented values.

## Slide 24
MIE 402 | ME LAB II
Conclusions, references, and appendices
Conclusions
Answer the objective with the key numerical result, supported limitation, and a useful improvement.
References
Cite sources where used. Include the lecture notes at minimum and list every cited source.
Appendices
Add supporting calculations or extra data only when needed. Keep essential evidence in the main text.
24
Notes: TIME: 38–39 minutes (1 minutes)
A conclusion should agree with the abstract and the figures. Do not introduce new results for the first time here. Mention what the experiment established within its tested range and what a repeat experiment should improve. The reference list is required, and the report needs in-text citations that connect borrowed equations, methods, or images to their sources. Appendices have no stated page limit but should be selective. The reader should be able to follow and evaluate the main argument without opening them.
SOURCE: Template for MIE 402 Report.docx
Report instructions: Template for MIE 402 Report.docx. Teaching examples labeled illustrative use invented values.

## Slide 25
MIE 402 | ME LAB II
Combined reports connect related experiments
Labs 2 and 3
Compare one angle with two coupled angles. Discuss model assumptions, initial conditions, and the limits of prediction.
Labs 4 and 5
Relate free-response frequency and damping to the forced response. Account for configuration changes.
Organization
Use one abstract and conclusion, with experiment-specific subsections and an explicit synthesis.
Suggested organization within the required template. Do not assume the page allowance doubles.
25
Notes: TIME: 39–40 minutes (1 minutes)
Students often produce a combined report by joining two independent documents. A more useful structure has one common objective and conclusion, with clearly labeled subsections for the experiment-specific methods and results. For the pendulums, compare what coupling and larger motions do to model agreement. For the cart experiments, test whether parameters estimated from a free decay help explain the forced response. The comparison is valid only when students account for any changed spring arrangement, damping, or mass. The assignment-specific page limit still controls.
SOURCE: Syllabus_MIE402_Fall26_6Labs.pdf and supplied Lecture 01
Report instructions: Template for MIE 402 Report.docx. Teaching examples labeled illustrative use invented values.

## Slide 26
MIE 402 | ME LAB II
The report rubric: ten equal criteria
Each criterion is 10% of the report grade | What to check
Complete sections / overall aesthetic | Required organization and consistent formatting
Clear figures / abstract | Readable evidence and a concise, quantitative summary
Data analysis / introducing the theory | Traceable processing and defined governing equations
Introducing the experiment / comparison with theory | Physical context and a fair model-data comparison
Discussion / meaningful results | Evidence-based interpretation and an answer to the objective
This table groups the ten original rubric criteria into pairs. Each individual criterion remains worth 10%.
26
Notes: TIME: 40–42 minutes (2 minutes)
Read the rubric as ten separate ten-percent items, even though this slide groups them into five rows. Completing all section headings accounts for only ten percent of a report. Formatting and figure quality matter, but so do the abstract, analysis, theory, experiment description, comparison, discussion, and meaningful results. Ask students to choose the weakest category in a report that has beautiful figures but no explanation of how frequency was estimated. The answer should include data analysis and potentially meaningful results. Use the rubric as a review checklist, not an invitation to repeat the same material in several sections.
SOURCE: Syllabus_MIE402_Fall26_6Labs.pdf
Report instructions: Template for MIE 402 Report.docx. Teaching examples labeled illustrative use invented values.

## Slide 27
MIE 402 | ME LAB II
Submission and integrity policies
27
DEADLINES
No late pre-labs.
Reports lose 25% for each day or partial day late.
INTEGRITY
Discuss approaches, but do not copy solutions or share MATLAB, Python, or Simulink files.
MAKE-UPS
Require instructor/GTA availability, space, and the correct equipment setup.
VERIFICATION
Any pre-lab or report may include a brief oral check of your understanding.
Notify the instructor during the first two weeks about approved conflicts or accommodation needs.
Notes: TIME: 42–43 minutes (1 minutes)
State the policy as written in the syllabus without inventing an additional penalty or AI rule. Any pre-lab or report may include a brief oral verification. Students should be able to explain their model, processing choices, and conclusions. Make-ups require instructor or GTA availability and the correct equipment. Notify the instructor within the first two weeks about approved schedule conflicts or accommodation needs. Canvas is the submission system and the place for section-specific updates.
SOURCE: Syllabus_MIE402_Fall26_6Labs.pdf and supplied Lecture 01
Report instructions: Template for MIE 402 Report.docx. Teaching examples labeled illustrative use invented values.

## Slide 28
MIE 402 | ME LAB II
Three-minute report exercise
Draft sentence
“The frequency was 1.47. Theory was 1.50. The error was small because of human error.”
Work with a neighbor
Add units, calculate the discrepancy, and separate the observation from its interpretation.
Then decide
What information is missing before you can judge agreement? Suggest one check that would help.
Invented teaching values. No submission is required for this in-class discussion.
28
Notes: TIME: 43–46 minutes (3 minutes)
Give students 45 seconds to work individually, 75 seconds to compare with a neighbor, and 60 seconds to share. Keep the debrief on the following slide hidden until they finish. Ask for one rewritten sentence, one missing uncertainty item, and one targeted check. Circulate or pause so the room actually has working time. If students finish early, ask whether agreement is independent when the model frequency was fitted to the same measured record. The objective is to practice a defensible claim, not to find a predetermined explanation for the discrepancy.
SOURCE: Syllabus_MIE402_Fall26_6Labs.pdf and supplied Lecture 01
Report instructions: Template for MIE 402 Report.docx. Teaching examples labeled illustrative use invented values.

## Slide 29
MIE 402 | ME LAB II
Exercise debrief
Results and comparison
The measured frequency was 1.47 Hz and the predicted frequency was 1.50 Hz. Their difference was 0.03 Hz, or 2.0% of the prediction.
Discussion
This discrepancy alone does not establish acceptable agreement. Timing and model-parameter uncertainties are needed.
Useful next check
Verify the time calibration and repeat the frequency estimate using a stated interval and method.
Other specific, evidence-based checks can also be valid.
29
Notes: TIME: 46–48 minutes (2 minutes)
Invite a student to read their sentence, then compare it with the example. Emphasize that two percent is a calculated discrepancy, not a universal pass criterion. A valid discussion separates what the data demonstrate from possible explanations. A check should target a mechanism that could change the result. For example, confirming the camera frame rate tests a timing-scale error. Repeating the estimate on several intervals tests stability of the estimate. These are more useful than a promise to be more careful. If time permits, ask which portions belong in Results, Comparison, and Discussion.
SOURCE: Syllabus_MIE402_Fall26_6Labs.pdf and supplied Lecture 01
Report instructions: Template for MIE 402 Report.docx. Teaching examples labeled illustrative use invented values.

## Slide 30
MIE 402 | ME LAB II
The first dates
30
SEP 9
Orientation
Course workflow and expectations
SEP 14
Measurement fundamentals
How to design and interpret measurements
SEP 21–25
Lab 1
Theory Monday; pre-lab due before your section
OCT 5
Lab 1 report
Submit on Canvas by 11:59 PM
There is no laboratory in Weeks 1–2.
Notes: TIME: 48–49 minutes (1 minutes)
Point to the current syllabus and remind students that the schedule is tentative. There is no laboratory during the first two weeks. The first laboratory week is September 21 through 25. The Lab 1 report is due October 5 at 11:59 PM. The other report dates in the syllabus are November 2 for Labs 2 and 3, December 7 for Labs 4 and 5, and December 14 for Lab 6. The syllabus places the December 7 due-date text in a November row, so read the explicit date and follow Canvas updates.
SOURCE: Syllabus_MIE402_Fall26_6Labs.pdf and supplied Lecture 01
Report instructions: Template for MIE 402 Report.docx. Teaching examples labeled illustrative use invented values.

## Slide 31
MIE 402 | ME LAB II
Preparation for Lab 1
31
BEFORE WEEK 3
• Confirm your laboratory section and GTA on Canvas
• Install or update MATLAB and Simulink
• Open the Lab 1 instructions and Pre-lab 1
• Know where and when your section meets
• Bring a way to save your experimental data
ONE QUESTION
What would make you trust an experimental result?
Questions & discussion
Notes: TIME: 49–50 minutes (1 minutes)
Close with one student answer to the opening trust question. A complete answer can mention the sampling rate, record duration, calibration, analysis method, model assumptions, and uncertainty. Ask students to locate the syllabus and report template before the next meeting. Remind them that public course materials are on GitHub and submissions, deadlines updates, and grades stay in Canvas. Leave any remaining seconds for a practical question about the first laboratory.
SOURCE: Syllabus_MIE402_Fall26_6Labs.pdf and supplied Lecture 01
Report instructions: Template for MIE 402 Report.docx. Teaching examples labeled illustrative use invented values.